## Slide 1: Inspiring IoT
A Glimpse into DIY Smart Homes
Boldizsár Bednárik
{ Electrical / Software Engineer :: Tech Enthusiast }
(STUFF)
github.com/bboldi/InspiringIoT

## Slide 2: Goals
Inspire, give directions where to start, share experience
Content
  Introduction / Little personal history
  Out of the box solutions the good the bad and the ugly
  Overview of a DIY smart system ( parts, protocols, hardware, software )
  NodeRED indtroduction
  Data logging and visualization

## Slide 3: Nothing but a dream …

## Slide 4: 2000s … Getting closer …
European Installation Bus (EIB)
communication protocol
install the necessary wiring and sockets

## Slide 5: Problems with EIB
Great! What's the issue? Reliable?
Hell yeah!!!!
Implementation? Price?
$1200
$400

## Slide 6: 2010s was a good period for DiY
esp8266
ESP-01 , ESP-12
$2 (!)
WiFi
First arduino
Later running code directly
Faster than arduino

## Slide 7: Welcome to the world of tomorrow!
Using ESPs for ~10 years in my projects
And you should too!

## Slide 8: Why Bother?
PRO
Limitless customization
Cost-Effective
Independence from Companies
  Price changes, subscriptions
  Privacy and Security
  Hacking ( zombie devices, spying )
  Support ( upgrades )
Constant support from the community
You can learn a TON!

## Slide 9: Structure
Nodes
Network (WiFi , Zigbee, etc)
Communication protocol ( MQTT )
Server ( hardware , software )
UI

## Slide 10: Network
WiFi
  Router
  2.4 GHz
Zigbee
  Router ( well … kind of )

## Slide 11: WiFi Nodes
Hardware
DIY
  ESP8266 or ESP32
  WemosD1 mini ( 8266 / 32 )
Off shelf ( moddable )
  Sonoff, athom.tech
RF wifi bridge ( sonoff ) (!)
Software
DIY - write your own firmware in C
Use open source
  EasyESP, EspHOME, Tasmota
Why not Raspberry pi for nodes?

## Slide 12: "Why not use raspberry pi?"

## Slide 13: Zigbee Nodes
Problems with 2.4GHz Wifi network
Zigbee Great Option!
DIY I don't think so …
Out of the box
No modding needed
Easy to connect to server
Cheap
No installation
Battery lasts forever
Zitbee2MQTT
CC2530

## Slide 14: Server - Hardware
Ideally a dedicated hardware, but can be a virtual machine on your home server ( if you have one )
Heart and soul of the Smart System
Raspberry Pi, Orange Pi, Banana Pi
Old PC / Laptop lying around
Cloud ( Linode , Digital Ocean, Hetzner )

## Slide 15: Server - OS ( btw I use Arch )
Windows? Might work … overkill TBH
Linux is King!
  Small, snappy
  Made for this - BEST for open source
  It's FUN
  Huge learning opportunity ( resources, tutorials, ChatGPT )

## Slide 16: Communication Protocol : MQTT
Special language devices use to talk
Small data packets/ header compared to http
Broker - Clients
Topics: Subscribe / Publish
Very efficient for small data packets
QOS
Mosquitto - open source
Message Queuing Telemetry Transport.

## Slide 17: NodeRED
"Brain" of the smart home
Alternatives: Domoticz, Home assistant, etc
My Personal preference
Flexible
Digital "lego" pieces called nodes
Data flow interaction
10C

## Slide 18: NodeRED - DEMO

## Slide 19: Logging and Visualization
Why?
Monitoring, Logging, Keeping values
Visualization of data
Can NodeRED do this?
InfluxDB + Grafana

## Slide 20: Logging: InfluxDB
Time series database
Designed to store / manage data that changes over time
Plays nicely with NodeRED
It has a query language, hard to visualize

## Slide 21: Visualization: Grafana
Native support for InfluxDB
Superb visualization
Dynamic dashboard
Alerting ( notifications, alerts, real time monitor )
You can connect other sources and visualize them on same dashboard

## Slide 22: My Experience …
Smart home hacking 10y , made lots of stuff
ESP , Zigbee + Open Source is reliable!
Except when it's not
Advice:
  use with caution for critical stuff
  always have a backup solution ( drop in replacement for heating, etc )
  implement failsafe ( physical thermostat for overheating )
  backup your data :) you might need it later!

## Slide 23: Examples, ideas
Heating , Cooling control depending on outside weather
Alarm system ( motion sensors, door sensors, detect who's home, presence detection , schedule )
Access control for your home with NFC, Moblie or Fingerprint
Smart home dashboard using old phone and node red dashboard
Automated curtain operation
Automated RGB light control ( wake up with light )
Connect camera system with your smart home ( rtsp with node red , save images, send it through )
Send notifications to phones ( Pushbullet, Pushover, etc )
Detect problems, like leakage and fire
Create your own voice assistant ( there's os alternative )
Connect everything with OpenAI ( chatgpt )
Endless possibilities …

## Slide 24: Thanks! Questions?
@bboldi
bbednarik@gmail.com
@bboldi
bboldi.com
https://www.youtube.com/@hellomakers
FEEDBACK